## Slide 1
HTGR Heat Application and Utilization
Andi Sofrany Ekariansyah
Follow Up Training Course on
Reactor Engineering and Safety:
High-Temperature Gas-Cooled Reactor
Yogyakarta, 18 - 22 May 2026

## Slide 2: Biodata
Nama : Andi Sofrany Ekariansyah
Kantor : Pusat Riset Teknologi Reaktor Nuklir (PTRKN)
Jabatan : Peneliti Madya - IVc
Kelompok Riset : Sistem keselamatan reaktor nuklir
Pendidikan:
  S1 Teknik Energi: Georg Simon-Ohm, Nurnberg, Germany 1997
  S2 Teknik Mesin - Konversi Energi: Universitas Indonesia, 2024
Pelatihan / Training:
  Longterm Training on Nuclear Safety and Safety Regulation 1997, Japan, 3 months
  Scientist Exchange Program, Japan, 2000 - 2001
  Study on Nuclear Desalination in Madura Island, Korea, 3 months -2002
  Instructor Training Course, Japan, 2 months - 2011

## Slide 3: Outline
PENDAHULUAN
Main Heat Applications of HTGR (prismatic and pebble bed)
Electricity heat generation from HTGR
Desalination from HTGR heat
Hydrogen production
Synthetic Fuel Production
Cogeneration (Combined Heat and Power)

## Slide 4
Pendahuluan
Mengapa HTGR dikembangkan?
Batasan kinerja reaktor daya konvensional
Temperatur · Efisiensi · Pemanfaatan Industri
Reaktor Daya Konvensional — Pendingin Air Ringan (LWR)
Moderator neutron
Massa H ≈ massa neutron
Perpindahan panas
Good HT properties, efektif & aman
Reaktivitas negatif
Umpan balik kuat
Kemudahan operasional:
Mudah diperoleh, disimpan, dipindahkan, dimurnikan
Air ringan dalam aplikasi Industri — Sudah Paten & Praktis
advantages
limitations

## Slide 5
Batasan kinerja fluida air ringan pada reaktor daya
Temperatur
Relatif rendah:
  PWR (290 – 330 °C, 155 bar),
  BWR (280 – 290 °C, 70 bar)
Efisiensi
LWR steam ~300 °C ≈ 573 K, condenser ~30 °C ≈ 303 K → ηmax ​≈1−303/573≈47%
High-T reactor ~900 °C ≈ 1173 K → ηmax ​≈1−303/1173≈74%
Water must stay liquid (especially in PWR) → requires high pressure
Material limits (corrosion, stress, fuel cladding like Zircaloy)
Safety margins against boiling crises and critical heat flux
Pemanfaatan industri
Fokus pada pembangkitan listrik
Desalination (dari listrik (RO) atau ekstraksi uap (MED, MSF)
Penerapan pada district heating (T ~ 70 – 150 °C)
Proses kimia temperatur rendah
Kebutuhan sumber energi temperatur tinggi untuk industri
Pendahuluan

## Slide 6
https://atomicinsights.com/history-promise-high-temperature-gas-cooled-reactors/
Pendahuluan

## Slide 7
Main Heat Applications of HTGR (prismatic and pebble bed)
Pembangkitan listrik
Desalinasi
Produksi hydrogen
Kogenerasi (panas dan pembangkitan listrik)
Produksi bahan bakar sintetis
Panas proses industri

## Slide 8
Electricity heat generation from HTGR
Direct Brayton Cycle (Gas turbine)
Indirect Brayton Cycle (with Intermediate HX)
Steam Rankine Cycle)
Combine Brayton – Rankine Cycle
Hot helium
turbine
Generator
Hot helium
Generator
IHX
(secondary gas)
Turbine
Hot helium
Generator
Steam generator (secondary water)
Turbine
Hot helium
Generator
Turbine
Steam generator (secondary water)
Generator
Turbine
GTTHTR300
Highest eff (45 – 50 %)
Direct turbine radiation exposure
Materials and maintenance concerns
Highest eff > 50 %
Max energy output
Eff 30 – 40 %
Proven technology

## Slide 9
Electricity heat generation from HTGR
Concept of GT Direct Brayton Cycle in THTR300
Concept of Simple Direct Closed Brayton Cycle
X. Qu et al. / Annals of Nuclear Energy 106 (2017) 185–194

## Slide 10
Electricity heat generation from HTGR
Concept of Rankine Cycle in HTR-PM
Concept of Simple Brayton-Rankine Cycle
X. Qu et al. / Annals of Nuclear Energy 106 (2017) 185–194
https://www.powermag.com/china-advances-htgr-technology/
Efficiency: 35 – 40 % 48 – 55 %
Complexity: low high
Heat utilization: moderate Excellent
Technology maturity: high medium
Turbine environment: steam (easy) Helium (challenging)

## Slide 11
Desalination from HTGR heat
Thermal coupling to thermal desalination plant
Hot helium
Intermediate loop
Desalination unit
Temperature reduction
700 – 900 °C
(radioactive)
Secondary coolant:
Water / steam
Molten salt
Clean helium
70 - 120 °C
Multi Effect Drsalination
Multi Stage Flash Desalination
Turbine
Generator
Reverse Osmosis
HXs
Electrical coupling to RO desalination plant
Thermal and electrical coupling to hybryd desalination plant

## Slide 12
Desalination from HTGR heat
Principal process of Multi Effect Distillation
Principal process of Multi Stage Flash Distillation
High temperature: 90 – 120 °C
10 – 30 stages (2 °C temperature drops)
Most intensive energy-intensive desalination
Low temperature: < 70 °C
high thermal efficiency, and high-quality distillate
Thermal Science and Engineering Progress 47 (2024) 102286

## Slide 13
Desalination from HTGR heat
Coupling Diagram of Hybrid MED-RO desalination unit from 600 MWth HTGR
Advances in Nuclear Power Process Heat Applications - IAEA-TECDOC-1682
Rx Power: 600 MWt
Rx pressure: 5.54 Mpa
Helium cycle:
Rx He in / out : 460 / 850 °C
Turbine T in / 0ut: 850 / 478 °C
Recuperator T in/out: 478 / 144 °C
Pre cooler T in/out: 144 / 33 °C
LP compressor T in/out: 33 / 123 °C
Intercooler T in/out: 123 / 35 °C
HP Compressor T in/out: 35 / 124 °C
Recuperator Tin/out: 124 / 460 °C

## Slide 14
Hydrogen production
Alkaline electrolysis
Heat, Eff: 70 – 75 %, CO2
Nuclear assisted Steam Methane Reforming
Grid power, Eff: 25 – 35 %
High-Temperature Electrolysis (HTE / SOEC)
HTGR heat, electricity, Eff: 40 – 60 %
Thermochemical Cycles (especially the Sulfur-Iodine Cycle)
HTGR heat, 42 – 52 %
Pebble bed HTR-PM China
Prismatic HTTR Japan
HTR-PM

## Slide 15
Hydrogen production
Solid Oxide Electrolizer Cell (SOEC)
Splitting 1 mol water (H₂O → H₂ + ½O₂) = 286 kJ/mol of total energy
At room water room temperature:
  237 kJ (electrical work) G
  49 kJ (heat work) T. S
At 800 °C steam temperature:
  164 kJ (electrical work) vs 122 kJ (heat work)
High-temperature SOEC require approximately 35–40 kWh of electricity to produce 1 kg of hydrogen when operated with steam (700 – 1000 °C): 20–30 % more efficient than low-temperature

## Slide 16
Hydrogen production
HTR-PM concept for High Temperature Electrolysis
Analysis of the viability of the 2 × 250 MWth HTR-PM project for the hydrogen production by the high temperature electrolysis and the Cu-Cl cycle. Int. J. Exergy, Vol. 34, No. 2, 2021

## Slide 17
Hydrogen production
Thermochemical Cycles (the Sulfur-Iodine Cycle)
Chemical reactions, not electrical splitting of water
High thermal efficiency predicted (about 50%)
Completely closed system without byproducts or effluents (besides hydrogen and oxygen)
Very high temperatures required (at least 850 °C (1,560 °F))
Corrosive reagents used : advanced materials needed for construction of process apparatus

## Slide 18
Hydrogen production
GTTHTR300C for SI Thermocycles Hydrogen Production
A hybrid HTGR system producing electricity, hydrogen and suchother products as water demanded in the Middle East. Nuclear Engineering and Design 271 (2014) 20–29
With Hydrogen W/O Hydrogen
Rx T outlet : 950 ° 850 °C
Rx pressure : 7 MPa 5 MPa
Mf core : 323 kg/sec 414 kg/sec
Grid power : 204 MWe 280 MWe
H2 power : 21.7 MWe
Heat input : 170 MWt
Hydrogen : 58 t/day (2400 kg/h)
Oxygen : 464 t/day

## Slide 19
Industrial Process Heat
Steel production by direct reduction iron
Using Hydrogen from HTGR heat
HTSE (SOEC)
SI Thermocycle
HTGR heat for
Hydrogen heating (reducing gas)
shaft furnace heating
Reduce emission
Iron ore (Iron Okside) oxygen removal in shaft furnace
Fe2​O3​+3H2​→2Fe+3H2​O
Metallic iron (direct reduced iron / DRI) and steam
Iron ore is converted into metallic iron without melting it in a blast furnace
Cement manufacturing
Oil refining and petrochemicals

## Slide 20
Synthetic Fuel Production
Biomass conversion
Coal gasification
Coal gasification system using nuclear heat for ammonia production. Applied Energy 67 (2000) 395±406
4 units reactor (@170 MWt) in parallel for 4 units coal gasification in series
Bottom process: C+H2​O→CO+H2
Upper process: CO+H2​O↔CO2​+H2
Process gas product: CO and H2 (syngas)
Gas process refineries →Synthetic fuels:
  Hydrogen
  Methanol
  H2 + Nitrogen → Ammonia (63 t/h)
  Synthetic natural gas
  Synthetic diesel and gasoline
Reduction of CO2 emissions by about 5x105 tons per year

## Slide 21
Cogeneration (Combined Heat and Power)
Conceptual Design of Electricity, Hydrogen, Desalination Cogeneration in HTR-PM
International Journal of Hydrogen Energy 4 8 ( 2023 )
Coupling the HTR-PM 2x250 MWth project with the SI cycle and the MSF process.
2 Rx power: @ 250 MWt (7 MPa)
T cold He: 250 °C
T hot He: 751 °C
Mf hot He: 96 kg/sec
Mf hot He for H2: 24 kg/sec
Mf hot He for electricity: 72 kg/sec
T hot He SG: 749.96 °C
T cold He SG: 199.73 °C
T steam: 571 °C (13.9 MPa)
T feed: 156 °C
Eff Rankine cycle:
WTu - WPmp / Q_SG = 44.18 %
Eff Rankine cycle, SI H2, MSF: 40.13 %
A study of ammonia-hydrogen-electricity cogeneration coupled to a very high-temperature heat source.
Nuclear Engineering and Design 414 (2023) 112585
HTTR

## Slide 22
Terima kasih