## Slide 1
BASIC CONCPET OF
NUCLEAR REACTOR SAFETY
Sutanto
Follow Up Training Course on
Reactor Engineering and Safety:
High-Temperature Gas-Cooled Reactor
Yogyakarta, 18 - 22 May 2026

## Slide 2: BIODATA
Nama : Sutanto
Unit Kerja : Poltek Nuklir BRIN
Pendidikan :
DIV Teknofisika Nuklir STTN-BATAN (2001-2005)
S2 Teknik Elektro UGM (2007-2009)
S3 Teknik Nuklir Universitas Waseda Jepang (2011-2014)
Bidang Keahlian : Instrumentasi kendali dan keselamatan reaktor

## Slide 3: OUTLINE
INTRODUCTION
BASIC SAFETY FUNCTION OF NUCLEAR REACTOR
DEFENCE IN DEPTH
ENGINEERED SAFETY SYSTEM
PASSIVE SAFETY

## Slide 4: INTRODUCTION
Fission reaction
Binding Energy of Atomic Nucleus
Fermi, 1942
Potential hazards:
Fission products  Sources of ionizing radiation
Safety systems:
Gravity driven fast shutdown rods
A secondary shutdown system made of buckets containing a cadmium sulphate solution (good neutron absorber)

## Slide 5: NUCLEAR FOR PEACE
“Atoms for Peace Speech” (1953)
D. Eisenhower
Former US President Eisenhower made “Atom for Peace Speech” in 1953 in the UN GA proposing establishment of IAEA
IAEA established in 1957 in UN system

## Slide 6: ACCIDENTS OF NPPs
“Nuclear power is by its very nature potentially dangerous, and … one must continually question whether the safeguards already in place are sufficient to prevent major accidents.” President’s Commission on TMI-2 (1979)
Stable reactor design  negative reactivity feedback
Deployment of passive safety system
TMI-2 Accident, 1979
Chernobyl Accident, 1986
Fukushima Accident, 2011

## Slide 7: TMI-2 ACCIDENT
Key Safety System & Components:
RCS & PORV
HPI System
Containment building
Auxiliary Feedwater System
Initiating event:
Loss of feedwater (Blockage)
Primary pressure increasing
Stuck open of PORV  LOCA
Operator did not realize it  human factors and reliability
Lesson learned:
Safety culture (operator training, testing, licensing, shift scheduling & overtime)
Concept of Defence in Depth
Stuck open
Blockage in resin transfer line

## Slide 8: ACCIDENTS CLASSIFICATION
Design Basis Accidents: Postulated events/accidents chosen in order to design all the plant system (particularly the safety system)
Example: Transients, Loss of coolant flow, LOCA, etc.
Beyond Basis Design Accidents: Extreme nuclear events that exceed the DBA
Severe Accidents: Accident conditions more severe than a DBA and involving significant core degradation

## Slide 9: THE INTERNATIONAL NUCLEAR AND RADIOLOGICAL EVENT SCALE

## Slide 10: NUCLEAR SAFETY OBJECTIVES
The radiation protection objective: To ensure in all operational states that radiation exposure within the plant is kept below prescribed limit & ALARA and to ensure mitigation of the radiological consequences of any accidents
The technical safety objective: To take all reasonably practicable measures to prevent accident in NPP; to ensure that any radiation consequences would be minor and below prescribed limits; and to ensure that the likelihood of accidents with serious radiological consequences is extremely low
Reference: Gianni P., 2006
The general objective: To protect individuals, society & the environment by establishing & maintaining effective defences against radiological hazards in NPPs

## Slide 11: BASIC SAFETY FUNCTION IN NPP
Shutting Down
Core Cooling
Radiation Confinement
Control rods, boron solution/injection, negative reactivity feedback
Emergency core cooling system, Residual heat removal, coolant injection
Physical barriers

## Slide 12: DEFENCE IN DEPTH
Definition: Creation of many, mutually independent, levels of defence against the initiation and the progression of accident.
Principle physical barriers
Five levels:
Good plant design (inherent safety)
Control systems
Emergency systems
Accident management
Emergency plans

## Slide 13: PHYSICAL BARRIERS: Water-Cooled Reactor (PWR)
5th barrier: reactor bulding
1st barrier:
Fuel pellet matrix
2nd barrier: Fuel cladding
3rd barrier: Reactor pressure boundary/RPV
4th barrier: Containment

## Slide 14: Fuel Matrix (PWR)
Material containing the nuclear fuel and retaining the fission products
Typically consisting of small, cylindrical pellets made of enriched uranium dioxide (UO2)
Ceramic material
Highly stable

## Slide 15: Fuel Cladding (PWR)
Zirconium alloys
Low absorption of neutrons
Excellent corrosion resistance
Efficient heat transfer
Helium gap: Space for fuel expansion

## Slide 16: Reactor Coolant System (PWR)
Components:
Reactor Pressure Vessel (RPV)
Coolant
Primary Coolant Loop
Pressurizer
Pumps
Heat Exchanger
Functions:
Heat Removal
Temperature Regulation
Pressure Maintenance
Barrier to Radioactive Release

## Slide 17: Containment Building (AP1000)
Robust, airtight structure
To prevent radioactive materials leakage to environment
Withstand to:
Seismic activity
Extreme weather conditions
Aircraft crashes
External explosions

## Slide 18: ENGINEERED SAFETY SYSTEM
Reactor shutdown: SCRAM & Boron injection
Safety principle of LWRs: Keeping water level
Safety principle of SCWR: Keeping core flow rate

## Slide 19: Emergency Core Cooling System/ Residual Heat Removal
SCRAM actuation due to an initiating event
Residual heat removal by using ECCS/RHR system
PWR
BWR

## Slide 20: Containment Spray System
Case of LOCA
Sprayed borated water
Installed heat exchanger to remove the heat

## Slide 21: Safety System of SCWR
SCRAM & SLCS
AFS (Auxiliary Feedwater System): Coolant injection in high pressure
LPCI: Low pressure coolant injection
ADS (Automatic Depressurization System)
Containment

## Slide 22: PASSIVE SAFETY SYSTEM

## Slide 23: Online Emergency Condenser

## Slide 24: Passive Pressure Pulse Transmitters

## Slide 25: INHERENT SAFETY FEATURE OF HTGR
Coated fuel particle with 4 ceramic layers as primary barriers
Moderator of graphite with large heat capacity
Negative reactivity feedback
Source: Nagasumi et al., 2026

## Slide 26: Cooling & Reactor Control System of HTGR

## Slide 27: SUMMARY
Nuclear power is by its very nature potentially dangerous. Research and development of enhancing the safety features of nuclear power plants are carried out continuously in the world
Concept of Defence in Depth optimizes the achievement of the nuclear safety objectives
In case emergency power are available, active engineered safety systems are effective for accident mitigations, but in case of station blackout, passive safety system is important to perform the safety function
A nuclear reactor with strong inherent safety feature has excellent safety performance

## Slide 28
Terima kasih